## Slide 1: Transducer
Md. Tariqul Islam
Lecturer, Dept. of EEE
Green University of Bangladesh

## Slide 2: Learning Outcomes
01. Definition and Classifications
What is transducer, what kinds of it.
02. Operating Principle
How does transducer works?
03. Election Criteria
How can we select the best quality of transducer?
04. Comparison among different transducer
Details classifications among different types of transducer
05. Applications
Uses of a transducer in a practical life.

## Slide 3: Introduction
What is transducer?
A transducer is a device which transforms a nonelectrical physical quantity (i.e. temperature, sound or light) into an electrical signal (i.e. voltage, current, capacity...).
In other word, it is a device that is capable of converting the physical quantity into a proportional electrical quantity such as voltage or current.

## Slide 4: How does transducer work?
Transducer contains two parts such as the sensing element and transduction element.
The sensing element is called as the sensor which is producing measurable response to change in physical conditions.
The transduction element converts the sensor output to suitable electrical form.

## Slide 5: ELECTION CRITERIA OF THE TRANSDUCERS
Operating principle: The transducers are many times selected on the basis of operating principle used by them. The operating principle used may be resistive, inductive, capacitive, optoelectronic, piezo-electric etc.
Sensitivity: The transducer must be sensitive.
enough to produce detectable output.
Operating range: The transducer should maintain the range requirement and have a good resolution over the entire range.
Accuracy: High accuracy is assured
Errors: The transducer should maintain the expected input-output relationship as described by the transfer function so as to avoid errors.
Environmental capability: It should be assured that the transducer selected to work under specified environmental conditions maintains its input- output relationship and does not break down.

## Slide 6
Insensitive to unwanted Signal: The transducer should be minimally sensitive to unwanted signals and highly sensitive to desired signals.
Stability: The transducer must be stable.

## Slide 7: Classification of Transducer
On the basis of the nature of the output signal
Transducers are divided into two categories such as analog transducer and digital transducer.
Analog Transducer: Analog transducers converts input signal into output signal, which is a continuous function of time. Example: Strain guage, Thermocouple etc.
Digital Transducer: Digital transducers converts input signal into the output signal in the form of pulses e.g. it gives discrete output.
Digital transducers are becoming more popular nowadays because of advantages associated with digital measuring instruments and also due to the fact that digital signals can be transmitted over a long distance without causing much distortion due to amplitude variation and phase shift.

## Slide 8: Classification of Transducer
On the basis of the method of applications
Transducers are divided into two categories. Such as primary transducer and secondary transducer.
Primary Transducer: When the input signal is directly sensed by the transducers and physical phenomenon is converted into the electrical form directly then such a transducer is called the primary transducer. For example: A THERMISTOR used for the measurement of temperature fall I this category. The THERMISTOR senses the temperature directly and causes the change in resistor with the change in temperature.
Secondary Transducer: When the input signal is sensed first by some detector or sensor and then its output being of some form other than input signal is given as input to a transducer for conversion into electrical from, them such a transducer falls in the category of secondary transducers. For example, in case of pressure measurement, bourdon tube is a primary sensor which converts pressure first into displacement. Then, the displacement is converted into an output voltage by an LVDT. In this case LVDT is a secondary transducer.

## Slide 9: Classification of Transducer
On the basis of methods of energy conversion used
Transducer may be classified into active and passive transducers.
Active transducer: The transducers which develop their output in the form of electrical voltage or current without any auxiliary source. Normally such transducers give very small outputs; therefore, use of amplifier becomes essential. For example TACHO generators used for measurements of angular velocity, thermocouples used for measurement of temperature, piezoelectric crystal used for measurement of force.
Passive Transducer: Transducers in which electrical parameters i.e resistance, inductance or capacitance changes with the change in input signal, are called the passive transducers. These transducers require external power source for energy conversion. In such transducers electrical parameters i.e. resistance inductance or capacitance causes a change in voltage, current or frequency of the external power source. For example resistive, capacitive, and inductive transducers.

## Slide 10: Thank you